A model reduction-based optimisation framework for large-scale simulators using iterative solvers

Ioannis Bonis and Constantinos Theodoropoulos*

School of Chemical Engineering and Analytical Science, The University of Manchester, Manchester M60 1QD, UK.

Abstract

A novel gradient-based optimisation framework for large-scale steady-state input/output simulators is presented. The method uses only low-dimensional Jacobian and reduced Hessian matrices calculated through on-line model-reduction techniques. The typically low-dimensional dominant system subspaces are adaptively computed using efficient subspace iterations. The corresponding low-dimensional Jacobians are constructed through a few numerical perturbations. Reduced Hessian matrices are computed numerically from a 2-step projection, firstly onto the dominant system subspace and secondly onto the subspace of the (few) degrees of freedom. The tubular reactor which is known to exhibit a rich parametric behaviour is used as an illustrative example.

Keywords: model reduction, input/output simulators, subspace iterations, reduced Hessian, double projection.

Introduction

Efficient design of complex partial differential equation-based non-linear chemical processes often leads to the constrained optimisation of large-scale nonlinear systems. Steady-state simulators of such large-scale systems are based on iterative solvers ranging from the well-known Newton-Raphson to advanced Newton-Krylov methods. Both deterministic (e.g. [1,2]) and meta-heuristic/stochastic (see e.g.[3]) methodologies have been developed for the optimisation of non-linear systems. Stochastic techniques rely on a large number of repeated calls to the system solver (function evaluations) and thus they are mostly used for moderate size combinatorial problems [3]. Furthermore, the gradient-based (deterministic) optimisation of large-scale problems is often problematic, involving long computational times and large memory requirements.  Especially in the case of black-box solvers (e.g. commercial simulators), where the system equations are not available to the user, optimisation becomes an even more tedious, if not impossible, task. We have recently developed model reduction-based methodologies for input/output large-scale and multi-scale dynamic simulators to handle both steady-state [4] and dynamic [5] deterministic optimisation. Here we extend these techniques for steady-state optimisation based on black-box steady-state simulators. The tubular reactor, a well-known distributed parameter system with a rich parametric behaviour, is used as an example to illustrate the developed methodologies.

The proposed optimisation algorithm

In this section we present our reduced input/output optimisation algorithm which is built around steady-state simulators which solve equations of the form:

(1)

Where  are the state variables,  are the decision variables (degrees of freedom) and  is twice differentiable.

Consider the following nonlinear optimisation problem:

s.t.   ,  and 	(2)

Where  is the objective function. This problem can be efficiently handled by the SQP method, which solves the Kuhn-Karush-Tucker optimality conditions using the Newton-Raphson method [1]. This is equivalent to solving a quadratic subproblem iteratively, with the kth iteration being:

,   	(3)

Where  is the Hessian of the system, is the search direction  and  is the vector of u and z. The space of the search direction can be written as the sum of subspaces,  and , where the columns of span the null space of . Hence,  can be expressed as:

(4)

where  and  are the components of  in the (small) space of the decision variables, z, and in the (large) space of the state variables, u, respectively. In reduced Hessian methods [2, 6] the calculation of the coordinate basis Z requires the construction and the inversion of the Jacobian,, of the system:

(5)

The problem (Eq. 3) is, thus, transformed to the unconstrained QP subproblem

(6)

The matrix ,  is the reduced Hessian and can be computed numerically, typically through Broyden updates. The corresponding Lagrange multipliers, λ, are computed from

(7)

The first term of Eq. 7 vanishes if feasible points (i.e. steady states) are computed at each iteration [6]. Clearly the calculation of the basis Z from Eq. 5 is expensive, as the large system Jacobians need to be constructed and inverted. Furthermore, in the case of input/output simulators Jacobians are not explicitly available to the optimisation procedure, or even to the solver itself as is the case of solvers using iterative linear algebra (e.g. Newton-Krylov solvers). In such cases the Jacobian can only be numerically approximated, with great computational expense in terms of CPU and memory requirements. For this purpose here we compute only reduced-order Jacobians of the dominant system subspace. Consider P the invariant subspace corresponding to the m rightmost eigenmodes of the system, which dominate the system’s behaviour. In most practical engineering problems m << n. The subspace P can be efficiently constructed through subspace iterations. In this work we employed the subroutine EB22, part of the HSL [7] to compute the basis of P . This subroutine performs subspace iterations on a matrix using efficient deflate-and-lock techniques to calculate its rightmost eigenvalues as well as basis vectors that span the subspace corresponding to the computed eigenvalues. The matrix itself is not explicitly required, only its products with other matrices or vectors, which can be calculated with directional numerical perturbations of the system’s residuals, thus enabling the algorithm to be used in conjunction with of black-box solvers. The reduced Jacobian ,   	(8)

can be efficiently computed through m numerical perturbations. We can easily extend to include the subspace of the degrees of freedom:

(9)

Also an approximation to the basis Z can be constructed using the reduced Jacobian H:

(10)

Where  and . It is, therefore, straightforward to show that

(11)

Hence Z* is the new coordinate basis constructed by a two-step projection, first onto the subspace of the dominant system eigenmodes and second onto the subspace of the (few) degrees of freedom. The reduced gradient of the objective function can be expressed as

(12)

The reduced Hessian can be computed from the new coordinate basis as:

(13)

Thus, a few numerical perturbations can be efficiently employed for its calculation. The corresponding reduced QP subproblem, defined by  Eq. 6 becomes:

(14)

is computed with only m Lagrange multipliers, i.e. the projection of the original multipliers onto P, which can be calculated:

(15)

In the current implementation of our algorithm feasible states (steady state solutions) are computed at the end of each iteration, so that the cross-terms  vanish.  Our proposed algorithm is outlined in Table 1.

Table 1. The proposed algorithm

| 1. | Choose initial guesses for x0 and B0 |
| --- | --- |
| 2. | Compute the steady state using an iterative solver and evaluate |
| 3. | Compute the basis : |
| 4. | Compute the reduced Hessian, , using |
| 5. | Solve the constrained QP subproblem: , |
| 6. | Calculate the Lagrange multipliers: after updating the reduced Jacobian |
| 7. | Update the solution: |
| 8. | Check for convergence. If convergence is not achieved go to (2). |

Case study: optimisation of  a tubular reactor

To illustrate the features of our proposed algorithm, we apply it to the case of a tubular reactor with axial dispersion, where an elementary first order irreversible exothermic reaction takes place:  [8]. The steady state problem is described two nonlinear partial differential equations (PDEs), which in dimensionless form are:

(16)

(17)

Here x1 and x2 are the dimensionless concentrations and temperatures. Da is the Damköhler number and y the dimensionless longitudinal coordinate. All the parameters are described in [5]. The boundary conditions are:

,    	(18)

The values of the parameters chosen are Le = 1.0, Pe1 = Pe2 = 5.0, γ = 20.0, β = 1.50, C = 12.0, x2w = 0.0. The PDEs were discretized using central Finite Differences, with 250 nodes, resulting in a system of 500 algebraic equations. We chose a single decision variable (namely Da) optimisation problem here in order to better characterise our method by visualising the optimisation path. Our objective was to maximise the exit dimensionless temperature x2. Despite the single degree of freedom, this is an interesting example since a number of bifurcations and multiple steady states, both stable and unstable exist. For the range of parameter values chosen, there are two turning points, at  and  and a Hopf point at.

Results and discussion

Optimisation with our proposed algorithm requires 9 iterations, so that  becomes less than 10-5. The size of the dominant subspace was m=10. All the required Jacobians and Hessians were computed through numerical perturbations using directly the solver as in the case of a black-box code. The optimisation path is depicted in Figure 1 and the relevant data for each iteration are shown in Table 2. Steady states, i.e. feasible points, were computed after each QP step. The lower bounds for all variables were 0, the upper bounds were 1 for  x1, 8 for x2 and 0.2 for Da. The overall computational times were reduced to several minutes compared with several hours when full Jacobians were numerically computed and reduced Hessians were calculated through Broyden updates as in the original method. The same optimisation problem was solved discretizing the PDE system in 500 nodes (1000 equations). The CPU time required for the optimisation of this “larger problem” (with m=10) was ~7.5 times higher than for the original problem. However, each call to the Newton solver requires approx. 8 times more CPU to solve the 500-node problem compared to the 250-node one. This leads to the conclusion that our algorithm scales well, since the overhead of the subspace calculations does not increase significantly as the size of the problem increases.

Table 2. Convergence data from the optimisation using the proposed algorithm

| Iteration |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 | 0.2000000 | 3.601851 | 71.46476 | 68.00314 |
| 2 | 0.1220243 | 3.447030 | 10865.52 | 7.930142 |
| 3 | 0. 1125917 | 5.112379 | 315.3314 | 17.40031 |
| 4 | 0. 1020631 | 7.328667 | 285.7956 | 21.09402 |
| 5 | 0. 1154800 | 6.120288 | 24.25304 | 5.963726 |
| 6 | 0. 1135797 | 6.082014 | 19.39071 | 3.127873 |
| 7 | 0. 1138771 | 6.055849 | 5.138073 | 0.05564 |
| 8 | 0. 1138730 | 6.054920 | 7.01∙10-2 | 7.80∙10-4 |
| 9 | 0. 1138732 | 6.054920 | 4.13∙10-3 | 4.59∙10-6 |

Conclusions

A novel model reduction-based optimization framework for input/output steady state simulators has been presented. It can be considered as an extension of Reduced Hessian methods. Reduced Hessians are efficiently computed through a double-step reduction procedure; first onto the dominant system subspace, adaptively computed through subspace iterations, and second onto the subspace of the decision variables. Only low-order Jacobians need to be computed through a few numerical perturbations, using only Reduced Hessians are computed  using m Lagrange multipliers, yielding more accurate updates than the BFGS method. We have applied this methodology in conjunction with a tubular reactor steady state simulator which was treated as a black box. The optimal values were accurately computed with efficiency, achieving significant speed-up compared with a brute-force approach computing full numerical Jacobians. We are planning to apply this methodology to large-scale commercial and state-of-the-art simulators which use solvers utilising iterative linear algebra.

Figure 1. (a) Bifurcation diagram solid (dashed) lines represent stable (unstable) steady states. (b) Optimisation path. Circles represent Newton steps and squares QP steps.

Figure 2. (a) Concentration and (b) temperature profile for Da=0.1 (dotted lines), Da=0.2 (dashed lines) and optimal Da=0.1138 (solid lines).

References

[1] T.F. Edgar, D.M. Himmelblau, 1988, Optimization of Chemical Processes, McGraw-Hill, NY

[2] L.T. Biegler, J. Nocedal and C. Schmidt, 1995, A Reduced Hessian Method for Large-Scale Constrained Optimization, Siam Journal on Optimization 5: 314-347

[3] C. Blum and A Roli, 2003, Metaheuristics in Combinatorial Optimization: Overview and Conceptual Comparison, ACM Computing Surveys, 35: 268-308.

[4] E. Luna-Ortiz and C. Theodoropoulos, 2005, An input/output model reduction-based optimization scheme for large-scale systems, Multiscale Modeling & Simulation 4: 691-708.

[5] C. Theodoropoulos and E. Luna-Ortiz, 2006, “A Reduced Input/Output Dynamic Optimisation Method for Macroscopic and Microscopic Systems”, in Model Reduction and Coarse-Graining Approaches for Multiscale Phenomena, A. Gorman, N. Kazantzis, I.G. Kevrekidis, H.C. Ottinger and C. theodoropoulos (eds) pp. 535-560.

[6] J. Nocedal and M. L. Overton, 1985, Projected Hessian updating algorithms for nonlinearly constrained optimization, SIAM Journal of Numerical Analysis, 22: 821-850.

[7] R. B. Lehoucq and J. A. Scott, 1996, An evaluation of software for computing eigenvalues of sparse nonsymmetric matrices, Technical report, Argonne National Laboratory. Argonne, IL.

[8] K. F. Jensen and W. H. Ray, 1982, The Bifurcation Behavior of Tubular Reactors, Chemical Engineering Science 37: 199-222.

# Footnotes

* Corresponding author, e-mail: k.theodoropoulos@manchester.ac.uk

# Text boxes

(a)				 	 (b)

(a)				 	 (b)