A Systematic Framework for Biorefinery Production Optimization

Norman E. Sammons, Jr.,a Wei Yuan,a Mario R. Eden,a Burak Aksoy,b Harry T. Cullinanb

aDepartment of Chemical Engineering, Auburn University,AL 36849, USA

bAlabama Center for Bioresource Engineering, Auburn, AL 36849, USA

Abstract

The integrated biorefinery has the opportunity to provide an independent and sustainable alternative for the production of bulk and fine chemicals. Because of the shift towards producing sustainable energy with minimal environmental impact, there is a need for a methodology capable of evaluating the integrated processes in order to identify the optimal set of products and production pathways. The complexity of the product allocation problem for such processing facilities demands a process systems engineering approach utilizing process integration and mathematical optimization techniques to ensure a targeted approach and serve as an interface between simulation work and experimental efforts. The objective of this work is to assist the bioprocessing industries in evaluating the profitability of different possible production routes and product portfolios while maximizing stakeholder value through global optimization of the supply chain. To meet these ends, a mathematical optimization based framework has been developed, which enables the inclusion of profitability measures and other techno-economic metrics along with process insights obtained from experimental as well as modeling and simulation studies. A case study has been included which highlights the robustness of the framework and its utility in decision making.

Keywords: Biorefining, sustainability, optimization, process modeling

Introduction

The process of separating biomass constituents and converting them to high value products is known as biorefining, and the integrated biorefinery provides a unique opportunity for reinvigorating an entire manufacturing sector by creating new product streams from a renewable resource [1]. Economic and environmental sustainability are achieved through the optimal use of renewable feedstocks, and a need exists for a process systems engineering (PSE) approach to ensure maximum economic and societal benefit through minimizing the usage of raw material and energy resources as well as the cost involved in supply chain operations intrinsic to biorefining. The bioprocessing industries are slowly becoming aware of the benefits of infusing PSE methods to this emerging field. To maximize the applicability of such systematic methods and to integrate experimental and modeling work, a unique partnership has been established consisting of researchers in academia and industry along with government entities, equipment vendors and industry stakeholders to procure the wide range of information necessary such as data needed for process simulation models, information on capacity constraints, financial data, and nonlinear optimization techniques. This information is obtained from a variety of collaborations involving industrial partners, internal academic partners in both chemical engineering and business, and external academic sources. This ensures that the data used in the decision making process is realistic and that the research addresses problems of industrial and regulatory interest. The overall goal of this work is to develop a system that will enable decision makers to evaluate different production pathways in biorefining in order to maximize value while measuring and minimizing environmental impact.

Methodology for Integrating Modeling and Experiments

In biorefining, the large number of possible process configurations and products results in a highly complex problem that cannot be solved using simple heuristics or rules of thumb. Business decision as well as policy makers must be able to strategically plan for and react to changes in market prices and environmental regulations by identifying the optimal product distribution and process configuration. Thus, it is necessary to develop a framework which includes environmental metrics, profitability measures, and other techno-economic metrics. Such a framework should enable policy and business decision makers to answer a number of important questions like:

For a given set of product prices, what should the process configuration be, i.e. what products should be produced in what amounts?

For a given product portfolio, how can process integration methods be utilized to optimize the production routes leading to the lowest environmental impact?

What are the discrete product prices that result in switching between different production schemes, i.e. what market developments or legislative strategies are required to make a certain product attractive?

What are the ramifications of changes in supply chain conditions on the optimal process configuration?

In the following sections, the developed framework for answering these questions is presented along with a discussion of some preliminary results.

The introduction of PSE methods into biorefining research provides a systematic framework capable of seamlessly interfacing results generated in simulation studies as well as experimental work. Such a framework is imperative when attempting to combine knowledge and information from a variety of research areas and disciplines. The objective of this approach is to create a library of rigorous simulation models for the processing routes along with a database of corresponding performance metrics. Wherever possible, experimental data is used to validate the performance of the simulation models, and for processes that commercial software packages are incapable of describing adequately, the performance metrics are initially based on experimental results until a satisfactory model has been developed.

Figure 1 shows a schematic representation of the strategy employed for identification of characteristic performance metrics of the individual subprocesses. The simulation models for each process are developed by extracting knowledge on yield, conversion, and energy usage from empirical as well as experimental data. If a given process requires the use of a solvent, molecular design techniques like CAMD and property clustering techniques are employed to identify alternative solvents that minimize environmental and safety concerns [2, 3].

Figure 1 – Strategy for identification of performance metrics.

Process integration techniques are then used to optimize the simulation models. This is an integral step in the model development as it ensures optimal utilization of biomass and energy resources. Finally, the optimized models are used to generate data for the economic as well as environmental performance metrics. The estimation of environmental performance is achieved through the use of the US-EPA Waste Reduction (WAR) algorithm [4]. It should be noted, that only the economic and environmental performance metrics are incorporated in the solution framework described below, thus decoupling the complex models from the decision making process. This approach allows for continuously updating the models as new data becomes available without having to change the selection methodology. Similarly, if new processes are to be included for evaluation, an additional set of metrics are simply added to the solution framework, thus making it robust and flexible.

Generalized Biorefinery Model

A generalized biorefinery model has been used to develop the structure of the optimization framework and is given in Figure 2. The model structure was formulated to include a variety of basic complexities encountered in the decision making process, e.g. whether a certain product should be sold or processed further, or which processing route to pursue if multiple production pathways exist for a given product. The objective function maximizing the overall profit of the biorefinery is illustrated in Equation 1.

Figure 2 – Generalized biorefinery model to illustrate possibilities in decision making tree.

(1)

Using this nomenclature, the first set of terms in Eq. (1) represents the sales revenue from the products made from each bioresource m. TSmk is a variable that denotes the production rate of product k from bioresource m that is sold to the market.  Cks is the sales price of product k which is a scalar and is determined through a survey of published prices and vendor quotes. The second set of terms represents the total processing cost incurred by the pathways pursued in production. Rmij is a variable that represents the processing rate of route ij while CmijP is a scalar that represents the cost of processing bioresource m through route ij and is determined through simulation models and process economics. The third set of terms represents the total cost of the biomass resource m, and this is broken down into the scalar purchase price of bioresource m in CmBM and the combined rate of biomass processed by the plant in Rm1j.  Although both TSmk and Rmij are variables in the optimization program, they are not independent since the variables are related via mass balance constraints around the product points.

The model may be utilized for short-term decision making with existing equipment and market arrangements, or long-term planning that will involve extensive capital expenditure, market forecasts on the future prospects of targeted products, and supply chain considerations. This generalized model, where the objective function and constraints are linear, is easily solved using commercially available software. It should be noted here that while earlier work such as the proposed solution by Sahinidis and Grossman incorporate process models into the optimization problem, the proposed framework separates the wide range of biorefining models from the optimization portion, thus reducing the complexity of the problem for the solver while maintaining the robustness achieved with proven optimization techniques [5].

Without including any constraints on capacity of the processing steps, the solution is a single-product configuration in which all available biomass is converted into the most profitable product. However, if constraints are imposed on the most profitable route, the framework identifies the additional products and processing routes required to maximize the overall profit, thus leading to a polygeneration facility [5]. Approximate capacity constraints are based on a variety of sources, e.g. existing equipment, vendor data and qualitative process information provided by academic and industrial collaborators. In order to effectively address the strategic planning objectives of business decision makers, it is necessary to incorporate the total capital investment as a constraint in the formulation. The capital investment for a given unit or process can be approximated as a function of its capacity or processing rate, and both linear and nonlinear expressions have been successfully implemented in the framework. Inclusion of capital cost constraints is crucial for practical application of the results, i.e. enabling evaluation of the potential benefits to be obtained for a given maximum investment by retrofitting an existing facility or constructing new plants.

Model Demonstration

Many adjustments were made to the parameters such as sales price, processing cost, processing rate conversions, and capital investment functions, and constraints were added on capacity as well as minimum and maximum sales quantities. These modifications were made to determine if the code would give the product distributions that were intuitively determined to maximize profit.  In every case, the code returned the solutions including predictable results on the product distribution as well as the pathways necessary to manufacture the product while maximizing value.

A case study was performed on a potential biorefinery involving the conversion of chicken litter to syngas, hydrogen, and electricity. Actual data on conversion rates were obtained from experimental work performed by the university and affiliated agencies as well as simulations constructed in ASPEN. Figure 3a shows the possible pathways for production and sale of these chemicals on the commodity market. The execution of the optimization code verified the results obtained from manual calculation; producing syngas from chicken litter and selling it on the market would maximize profit due to the high costs involved in converting the syngas to hydrogen or electricity. Figure 3b illustrates the active pathway chosen by the optimization program. This simple case study will be expanded to include a much wider range of products, production pathways, and feedstocks in order to become a crucial decision support tool in the emerging field of biorefining.

Figure 3 – Illustration of case study. (a) Unsolved decision making tree with variable designations. (b) Solved decision making tree with flowrate values and objective function.

Conclusions and Future Work

A general systematic framework for optimizing product portfolio and process configuration in integrated biorefineries has been presented. Decoupling the process models from the decision-making framework reduces problem complexity and increases robustness. The next phase of this work involves development of additional process models for the generation of performance metrics, specifically information on conversion, yield, and production cost for economic metrics and data to be used to generate a measure of environmental impact.  From there, process integration will be utilized to optimize the process models by reducing energy usage, material consumption, and waste streams.

An alternative formulation of the product allocation problem will be developed using a combination of general disjunctive programming (GDP) with the use of genetic algorithms (GA) as proposed by Odjo et al [7]. The current formulation of the problem is a mixed-integer nonlinear problem (MINLP), and the use of GA and GDP has been shown to solve nonconvex, discontinuous optimization problems more efficiently than the iterative MILP-NLP approach used in many solver programs. The computation time and objective values of optimal solutions between the GA-GDP solution method and the MINLP method will be compared to determine which formulation and solution style is more effective in solving this general problem [6].

The framework will also become a stronger financial tool through the incorporation of various economic ideas and analyses.  The use of net present value as a profitability measure in a similar fashion to Sahinidis and Grossmann will enable the inclusion of the cost of capital, interest expenses, depreciation, and tax consequences of pursued decisions [5]. The development of qualitative predictive models for capital investment and inclusion of capital amortization into the objective function will also increase the strength of the framework. Incorporation of options theory into the framework will allow management to develop financial strategies in response to events in the market or legislative environment. Finally, optimization under uncertainty will be studied to quantify the effects on process configuration resulting from minute changes in product prices [7]. This, in combination with implementing superstructure generation techniques, will lead to increased robustness of the methodology and thus better recommendations [8].

References

1.	Bridgwater, A.V. (2003). Renewable fuels and chemicals by thermal processing of biomass. Chemical Engineering Journal, 91, 87-102.

2.	M. R. Eden, S. B. Jørgensen, R. Gani and M. M. El-Halwagi. (2004). A novel framework for simultaneous separation process and product design. Chemical Engineering and Processing, 43, 595-608.

3.	P. M. Harper and R. Gani. (2000). A multi-step and multi-level approach for computer aided molecular design. Computers and Chemical Engineering, 24, 677-683.

4.	D. M. Young and H. Cabezas. (1999). Designing sustainable processes with simulation: the waste reduction (WAR) algorithm. Computers and Chemical Engineering, 23, 1477-1491.

5.	N. V. Sahinidis, I. E. Grossmann, R. E. Fornari and M. Chathrathi (1989). Optimization model for long range planning in the chemical industry. Computers and Chemical Engineering, 13, 1049-1063.

6.	A. Odjo, N. Sammons, A. Marcilla, M. Eden and J. Caballero. (2007). A disjunctive-genetic programming approach to synthesis of process networks. Computers and Chemical Engineering (in preparation).

7.	I. Banerjee and M. G. Ierapetritou. (2003). Parametric process synthesis for general nonlinear models. Computers and Chemical Engineering, 27, 1499-1512.

8.	A. Chakraborty and A.A. Linninger. (2003). Plant-wide waste management 2: Decision making under uncertainty. Industrial and Engineering Chemical Research, 42, 357-369.