Anhydrous Bioethanol for Fuels and Chemicals – Evaluations of Alternative Distillations and Solvents

Marina O.S. Dias,a Fabian A.D. Mateus,a Rubens Maciel Filho, a Maria R.W. Maciel, a Carlos E.V. Rossell b

a School of Chemical Engineering, State University of Campinas, UNICAMP, P.O. Box 6066, 13083-970, Campinas – SP, Brazil

bInterdisciplinary Center for Energy Planning, State University of Campinas, UNICAMP, P.O. Box 6192, 13400-970, Campinas – SP, Brazil

Abstract

The rise in oil prices and the attempt to diminish greenhouse gas emissions have encouraged the use of bioethanol as an additive or even a substitute to gasoline. Since water forms an azeotrope with ethanol at a concentration of about 89 % ethanol (mole basis) at 1 atm, conventional distillation can not achieve the necessary specification that allows its addition to gasoline. Different processes may be used for anhydrous bioethanol production; the most common in large scale in Brazil are azeotropic distillation with cyclohexane, extractive distillation with monoethyleneglycol (MEG) and adsorption on molecular sieves.

In this work, UniSim Design process simulator was used to simulate azeotropic and extractive distillation processes for anhydrous bioethanol production. Cyclohexane and n-heptane were used as solvents in azeotropic distillation, while MEG and glycerol were used in extractive distillation processes. Different configurations were analyzed, and results showed that extractive distillation processes have lower energy consumption than azeotropic distillation processes.

Results showed that bioglycerol, a by-product of biodiesel production, may be used as a solvent in extractive distillation process, replacing MEG, a fossil and toxic solvent, in the production of a high quality bioethanol, with no traces of solvent, similar energy consumption and solvent and ethanol losses, thus improving bioethanol production process sustainability.

Keywords: Bioethanol, Azeotropic Distillation, Extractive Distillation, Glycerol based solvent.

Introduction

The rise in oil prices and the need to diminish greenhouse gas emissions have encouraged the use of bioethanol as an additive or even as a substitute to gasoline all around the world. Also, bioethanol can be used as a basic pillar feedstock for driving a full renewable chemical industry. In order to be used either as an additive for gasoline or in some chemical feedstock route, ethanol produced from fermentation of glucose, obtained at a concentration around 4 % (molar basis), must be concentrated to about 98.5 % (molar basis, 99.3 % mass basis).

Since ethanol forms an azeotrope with water at a concentration of about 89 % at 1 atm, conventional distillation can not achieve the necessary product specification.

In this work, different solvents and configurations of both azeotropic and extractive distillation processes are considered and evaluated using process simulator UniSim Design. In all cases, the processes are simulated considering production of 1000 m³/day of anhydrous bioethanol and optimal operating conditions. The use of an alternative solvent, bioglycerol, a byproduct of biodiesel production, is proposed and its behavior is evaluated in terms of energy consumption and ethanol and solvent losses.

Azeotropic Distillation

Simulations of Azeotropic Distillation processes were carried out using the well known NRTL as the activity coefficient model for the liquid phase and the equation of state SRK for the vapor model. Stage numbering increases towards the top of the columns. Binary coefficients between solvent and water are not available at UniSim database and must be estimated. In the decanter, the estimation method used was UNIFAC-LLE, while in the other parts of the simulation UNIFAC-VLE was considered. An extensive thermodynamic behavior study was made and the comparison with experimental data showed that these models are suitable ones.

In the azeotropic distillation process, a solvent-rich solution is supplied on the top of the azeotropic column, and hydrated bioethanol (liquid phase) and alcohol recycle are supplied in a stage below the top. On the top of the azeotropic column, a ternary azeotrope is obtained, while anhydrous bioethanol is withdrawn at the bottom. The ternary azeotrope is cooled and two liquid phases are obtained in the decanter: an organic phase, which is recycled to the azeotropic column, and an aqueous phase, which is separated in the recovery column. At the top of the recovery column, an alcoholic solution is obtained and recycled to the azeotropic column, while nearly pure water is obtained at the bottom. A solvent make-up stream is supplied in order to recover some solvent lost. Process configuration is shown in Figure 1.

Figure 1: Configuration of Azeotropic Distillation process.

Two different solvents were studied for anhydrous bioethanol production by azeotropic distillation: cyclohexane and n-heptane. The anhydrous bioethanol produced by azeotropic distillation contains traces of solvent. If the bioethanol is to be used as an additive for gasoline, traces of n-heptane would not affect the quality of the blend, in contrast with traces of cyclohexane.

In the process with n-heptane, a different configuration was studied. It consists of another condenser on top of the azeotropic column. The best conditions were verified in this configuration.

A study of the optimal feed stage and temperature in the decanter for each process was made. In Table 1, parameters are presented for the azeotropic distillation with cyclohexane and n-heptane, as well as with n-heptane with azeotropic condenser.

Table 1: Parameters for the azeotropic distillation process with cyclohexane and n-heptane, and n-heptane with condenser(*) in the azeotropic column.

| Parameter | Cyclohexane | n-Heptane | n-Heptane* |
| --- | --- | --- | --- |
| Number of stages - Azeotropic Column | 30 | 35 | 30 |
| Solvent-rich solution feed stage | 30 | 35 | 30 |
| Solvent temperature (°C) | 50 | 30 | 30 |
| Hydrated Bioethanol feed stage | 26 | 28 | 24 |
| Solvent-rich solution flow (kmol/h) | 6156 | 4620 | 2725 |
| Hydrated Bioethanol flow (kmol/h) | 850 | 850 | 850 |
| Alcohol recycle flow (kmol/h) | 4916 | 2345 | 1921 |
| Anhydrous Bioethanol flow (kmol/h) | 723 | 723 | 723 |
| Azeotropic Column Bottom Temperature (°C) | 78 | 78.1 | 78.1 |
| Number of stages - Recovery Column | 16 | 23 | 23 |
| Heavy phase feed stage | 14 | 13 | 13 |
| Water in water stream (% mol) | 99.9 | 99.9 | 99.9 |
| Recovery Column Reflux Ratio | 0.75 | 2 | 2 |
| Recovery Column Bottom Temperature (°C) | 99.4 | 99.7 | 99.7 |
| Azeotropic Column Reboiler Duty (kW) | 111,116 | 84,435 | 90,993 |
| Recovery Column Reboiler Duty (kW) | 96,175 | 80,957 | 66,375 |
| Bioethanol losses (%) | 0.017 | 0.017 | 0.017 |
| Solvent losses (%) | 0.001 | 0.003 | 0.008 |

Simulations showed that n-heptane is an interesting option to be considered for industrial implementation. Energy consumption of the processes with n-heptane is lower than the one using cyclohexane, and solvent and ethanol losses are similar. The use of additional equipment, the condenser, provides a reduction in energy consumption.

Extractive Distillation

Conventional Extractive Distillation Process

Conventional Extractive Distillation process uses two distillation columns to separate the binary azeotrope ethanol-water. The first one is called extractive column and provides pure ethanol at the top. The second one is called recovery column and separates the water-solvent mixture coming from the first column. In the case of glycerol, the recovery column must operate at sub atmospheric pressures (50 kPa) to avoid solvent decomposition, since it decomposes into acrolein when heated above 280°C (Young, 2003), which is below its boiling point at atmospheric pressure.

Simulations of Extractive Distillation process were carried out using UNIQUAC as the activity coefficient model for the liquid phase and equation of state SRK for the vapor model. Stage numbering increases towards the top of the columns (reboiler is considered stage 0). Hydrated ethanol, with 93 % (mass) ethanol, is supplied as a saturated vapor near to the bottom of the extractive column, while recycled solvent is cooled and supplied near to the top. The mixture solvent-water coming from the extractive column is separated in a recovery column. Configuration of the conventional extractive distillation process is depicted in Figure 2.

Figure 2: Configuration of Conventional Extractive Distillation Process.

Extractive Distillation process with monoethyleneglycol (MEG) was implemented on industrial scale for production of anhydrous bioethanol in Brazil in 2001 (Meirelles, 2006). The process simulation considered in this work involves an optimization of the process used in industry: hydrated bioethanol is supplied as saturated vapor, since it can be obtained in vapor phase in the conventional distillation process. In the conventional industrial process hydrated ethanol is obtained in condensed phase and vaporized prior to extractive distillation process.

Glycerol was used in the 1950s as solvent in an absorption process for producing anhydrous ethanol (Mariller, 1950), but its high consumption of energy and the lack of suitable automation and control available in that period forced the search for alternatives and the process with glycerol was abandoned. Considering the increase on availability of bioglycerol, that is, glycerol obtained as a by-product of biodiesel production, its use as a solvent for extractive distillation is proposed in this work. The use of bioglycerol in extractive distillation process for anhydrous bioethanol production is under patent solicitation and would replace a toxic and fossil solvent (MEG), thus improving bioethanol production process sustainability.

Design parameters, reboiler duty and solvent and bioethanol losses of the conventional extractive distillation process using MEG and glycerol as solvents are shown in Table 2.

In the conventional extractive distillation process, energy consumption of the process with glycerol is only 1.15 % greater than that with MEG. Bioethanol and solvent losses are similar.

Alternative Extractive Distillation Process

An alternative configuration of the extractive distillation process eliminates the recovery column (Brito, 1997): pure water can be removed by one side stream, while ethanol is produced at the top and solvent at the bottom. The configuration of the alternative extractive distillation process is shown in Figure 3.

In Table 3, design parameters, reboiler duty and solvent and bioethanol losses of the alternative extractive distillation process using MEG and glycerol as solvents are presented. The extractive column with glycerol must operate at 60 kPa to avoid decomposition. In the proposed alternative process energy and solvent consumption, bioethanol and solvent losses are larger than those of the conventional processes, but the operation in a single column gives rise to lower equipment, operational and control costs (intensified process) when compared to conventional process.

Table 2: Parameters of the conventional extractive distillation process with MEG and glycerol.

| Parameter | MEG | Glycerol |
| --- | --- | --- |
| Number of stages of the Extractive Column | 35 | 35 |
| Solvent feed stage Solvent temperature (°C) Hydrated Bioethanol feed stage Extractive Column Reflux Ratio Solvent flow (kmol/h) Hydrated Bioethanol flow (kmol/h) Anhydrous Bioethanol flow (kmol/h) Extractive Column Bottom Temperature (°C) | 31 140 9 1.2 260 847 723 133.7 | 31 130 12 0.97 259 847 723 152.8 |
| Number of stages of the Recovery Column | 10 | 10 |
| Solvent + water feed stage | 6 | 6 |
| Water concentration in water vapor stream (% mol) Recovery Column Reflux Ratio Recovery Column Bottom Temperature (°C) | 99.98 0.18 197.2 | 99.98 0.01 259 |
| Extractive Column Reboiler Duty, Reb-1 (kW) | 7463 | 6668 |
| Recovery Column Reboiler Duty, Reb-2 (kW) | 2588 | 3540 |
| Bioethanol losses (%) | 1.10-5 | 1.3.10-5 |
| Solvent losses (%) | 0.01 | 0.01 |

Figure 3: Configuration of Alternative Extractive Distillation Process.

Energy consumption of the alternative processes with glycerol is 15 % larger than that with MEG, but solvent losses are 25 times lower and only 4.2 % larger than that of conventional process with MEG.

Simulations of the process in a single column showed that the process with MEG is much more unstable than that with glycerol: small changes in operating conditions, such as reflux ratio and water side stream flow, cause great changes in solvent and ethanol losses, opposed to the process with glycerol. The extractive distillation process allows the production of anhydrous bioethanol with no traces of solvent,  hence suitable for use as fuel or in food and pharmaceutical industries.

Table 3: Parameters of the alternative extractive distillation process with MEG and glycerol.

| Parameter | MEG | Glycerol |
| --- | --- | --- |
| Number of stages of the Extractive Column | 35 | 35 |
| Solvent feed stage Solvent temperature (°C) Hydrated Bioethanol feed stage Water vapor outlet stage Extractive Column Reflux Ratio Solvent flow (kmol/h) Hydrated Bioethanol flow (kmol/h) Anhydrous Bioethanol flow (kmol/h) Extractive Column Bottom Temperature (°C) Extractive Column Reboiler Duty, Reb (kW) Water concentration in water vapor stream (% mol) Bioethanol losses (%) Solvent losses (%) | 32 100 14 5 0.96 300 848 724 197.2 9074 98.79 9.10-5 0.49 | 32 130 14 4 0.92 309 847 723 269.4 10480 99.95 6.10-5 0.02 |

Conclusions

Simulations of the azeotropic distillation processes are much more unstable and complex than those of the extractive distillation processes. Results showed that energy consumption on reboilers and bioethanol losses are lower in the case of extractive distillation processes with both MEG and glycerol as solvents.

If bioethanol is to be used as a gasoline additive, the replacement of cyclohexane in azeotropic distillation process by n-heptane seems to be an interesting option, since traces of this solvent would not affect the quality of the fuel (gasoline-ethanol blend), as  opposed  when cyclohexane is used. The modifications necessary to change the process with cyclohexane to n-heptane are small and easily implemented.

The extractive distillation process in one side stream column with glycerol shows a large potential for industrial application. Glycerol availability is expected to increase, since it is a by-product of the production of biodiesel. It makes its use even more interesting since it leads to decrease the dependence on fossil derivates. Besides the significant environmental advantages, this process may use only one distillation column, with decrease on operating costs.

Acknowledgments

The authors acknowledge FAPESP and CNPq for financial support.

References

R.P. Brito, M.R.W. Maciel, A.J.A. Meirelles, 1997. New extractive distillation configuration for separating binary azeotropic mixtures. In: The First European Congress of Chemical Engineering, Italy, 1, 1333-1336.

C. Mariller, 1950. Destilación y rectificación de los liquidos industriales, 530.

A.J.A. Meirelles, 2006. Expansão da Produção de Bioetanol e Melhoria Tecnológica da Destilação Alcoólica. In: Workshop “Produção de Etanol”, Lorena.

J.A. Young, 2003. CLIP: Glycerol, Journal of Chemical Education, 80, 25.