## Slide 1: P8
Tranformed inputs
Briefly on pro and cons of MPC
RTO
ESC

## Slide 2: Nonlinear feedforward, decoupling and linearization
Tranformed inputs: Extremely simple and effective way of achieving feedforward, decoupling and linearization

## Slide 3: Feedforward control
Feedforward control relies on model
as opposed to feedback which relies mostly on data
Feedback control: Linear model is often OK
Feedforward control: Much less likely that linear model is OK because of process changes and disturbances
Here: Nonlinear feedforward control using Input transformations based on static process model

## Slide 4
STATIC MODEL IS OFTEN OK, even for linear feedforward:

## Slide 5: Use of transformed inputs
Transformed input v =g(u,w,y,d)
Replaces the physical input u for control of y.
Aim: Transformed system is easier to control
  May include:
    Decoupling
    Linearization
    Feedforward
Examples
  v = u/d (ratio control for feedforward)
  v = u1/u2 (ratio control for decoupling)
  v = u1+ d (from mass balance)
  v = w(u,d) = F
Input calculation block: Inverts g to find resulting u
  u = v*d
  u1 = v*u2
  u1 = v – d
  Flow controller finds u for given v=F by feedback (cascade control)
Controller
C
(dynamic)
Process
(dynamic)
ys
u=
g-1(v,..,d)
y
d
w
Input calculation
(Static calculation block that inverts g)
y
v =g(u,w,y,d)
=transformed input
Transformed system

## Slide 6: Systematic approach for finding transformed inputs from static model
Static model:
Define = (so v0=g=RHS of steady-state model. Extremely simple!)
Invert by solving with respect to for given : (14)
Transformed system:
Decoupled () , linear and independent of d !!!!!!
Ideal case v0=ys. So feedback controller C corrects for model error and unmeasured disturbances.
y = controlled variable (main output)
w = measured state (output) which is treated as measured disturbance (for example, a recycle flow in a process)

## Slide 7: Example: Blending process
Static material balances, :
Solve for
This can be implemented directly and give y=v0.
Alternative simple implementation. Solving (16a) with respect to F1 and (16b) with respect to F2 gives:
(16)
(18)
Transformed inputs
(17)

## Slide 8
(11)

## Slide 9: Also: Transformed outputs z
No fundamental advantage, but can simplify input transformation
For example, y=T, z=H (enthalpy)

## Slide 10: More on transformed inputs

## Slide 11: MPC and RTO

## Slide 12: What about MPC?
First industrial use in the 1970s
Became common in the refining and petrochemical industry in the 1980s
In the 1990s a bright future was predicted for MPC in all industries (chemical, thermal power, …)
30 years later: We know that this did not happen (yes, it is used in other industries, but much less than some predicted)
Why? First, the performance benefits of MPC compared to ARC are often minor (if any)
In addition, MPC has some limitations
  Expensive to obtain model
  Does not easily handle integral action, cascade and ratio control
  Normally, cannot be used at startup (so need ARC anyway)
  Can be difficult to tune. Difficult to incorporate fast control tasks (because of centralized approach)
  Computations can be slow
  Robustness (e.g., gain margin) handled indirectly
Advantages of MPC
  Very good for interactive multivariable dynamic processes
  Coordinates feedforward and feedback
  Coordinates use of many inputs
  Makes use of information about future disturbances, setpoints and prices (predictive capabilities of MPC)
  Can handle nonlinear dynamic processes (nonlinear MPC)
What about constraints
  Not really a major advantage with MPC; can be handled well also with ARC
MPC = model predictive control
ARC = advanced regulatory control

## Slide 14: Optimal operation and constraints switching
We have presented effective decentralized approaches for constraint switching (MV-MV, CV-CV, MV-CV).
  Optimal in many cases, but not in general
  For example, may not be able to cover cases with more than one unconstrained region More than one self-optimizing variable
An alternative is model-based RTO, usually based on static model
RTO = Real-time optimization

## Slide 15: Economic real-time optimization(RTO) Alternative RTO approaches:
Model-based
Separate RTO layer (online dynamic or steady-state optimization)
Feedback-optimizing control (put optimization into control layer)
    Alt.1. (Most general): Based on dual decomposition (iterate on Lagrange multipliers λ)
    Alt.2 (Tighter constraint control): Region-based with reduced gradient
Data-based
Hill-climbing methods = Extremum-seeking control (model free. But need to measure cost J)

## Slide 16: I. Conventional (commercial) steady-state RTO
Fairly common in refining and petrochemical industy.
Two-step approach:
Step 1. “Data reconciliation”:
  Steady-state detection
  Update estimate of d: model parameters, disturbances (feed), constraints
Step 2. Re-optimize to find new optimal steady state
Data reconciliation

## Slide 17: Steady-state wait time
Transient measurements cannot be used  system must “settle”
Large chunks of data discarded
Steady state detection issues
  Erroneously accept transient data
  Non-stationary drifts

## Slide 18: How to avoid steady state wait time?
1. Dynamic RTO = EMPC

## Slide 19: How to avoid steady state wait time?
2. Hybrid RTO
Static

## Slide 20: RTO problem
Steady-state RTO (used in Hybrid RTO):
s.t.:
Dynamic RTO ≡ (Economic) nonlinear MPC :
s.t.:
Now we calculate not only an optimal point, but an optimal trajectory!’
BUT Much more complex that static RTO, and may not give much economic benefit

## Slide 21: II. Feedback RTO (unconstrained case)
«Solving RTO-problem using PI control»
Unconstrained optimization.
Necessary condition of optimality (NCO):
  Gradient of cost function = 0
  0
Feedback RTO

## Slide 22: II. Feedback RTO (unconstrained case)
D Krishnamoorthy, E Jahanshahi, S Skogestad. Feedback Real-Time Optimization Strategy Using a Novel Steady-state Gradient Estimate and Transient Measurements. Industrial & Engineering Chemistry Research, 2019
Linearize the dynamic model
Trick, set
Gradient estimator
Note: This is one simple way of doing the gradient estimation
Kalman Filter
Feedback RTO

## Slide 23
Constrained optimization problem
Solution: Turn into unconstrained optimization problem
using Lagrange multipliers
minu,λ L
  u = primal variables = inputs
  λ ≥ 0 = dual variables = Lagrange multipliers = shadow prices
Necessary conditions of optimality (KKT-conditions)
J
(complementary condition)
Master
Single-loop PI controllers
Alt.1A: Feedback implementation using dual decomposition and feedback control to compute u (Krishnamoorthy, Dirza, Skogestad)
J
Alt.A. Use controllers also here
II. Feedback RTO (with constraints)
Feedback RTO

## Slide 24
Master
Single-loop PI controllers
Alt.1A: Feedback implementation using dual decomposition and feedback control to compute u (Krishnamoorthy, Dirza, Skogestad)
Alt.A. Use controllers also here
«Primal-dual feedback control»
Makes use of «dual decomposition» of constrained optimization
Selector on dual variables λ
Very nice for cases with shared utility g, for example steam plant
  Local cost: Li = Ji + λ gi
Problem 1: Constraint control on slow time scale (upper layer)
  Can be fixed using override at bottom of hiearchy (Risvan Dirza)
Problem 2: Alt.A Single-loop control in lower layer (Lu=0) may not be possible for coupled processes so may need to use Alt. B.
Feedback RTO
II. Feedback RTO (with constraints)

## Slide 25: Alternative 1B: Dual composition with optimization/solver for computing u (primal variables)
«Optimal Resource Allocation using Distributed Feedback-based Real-time Optimization». Risvan Dirza, Sigurd Skogestad, Dinesh Krishnamoorthy. IFAC Adchem Conference, 2021
λ = Lagrange multipliers = shadow prices = dual variables
Process
Unconstrained optimization
(nu PID-controllers or solver)
Gradient estimator
Constraint control
(nc slower PI/I-controllers)
MAX
0
y
g (measured constraint)
g (measured constraint)
SP=0
SP=0
u
d
Dual variables
Primal variables
Alt.B. Use solver here
Filter
Feedback RTO
«Primal-dual feedback control»
Makes use of «dual decomposition» of constrained optimization
Selector on dual variables λ
Very nice for cases with shared utility g, for example steam plant
  Local cost: Li = Ji + λ gi
Problem 1: Constraint control on slow time scale (upper layer)
  Can be fixed using override at bottom of hiearchy (Risvan Dirza)
Problem 2: Alt.A Single-loop control in lower layer (Lu=0) may not be possible for coupled processes so may need to use Alt. B.
Alt.B: May need to add filter to avoid instability

## Slide 26: Alternative 2: Region-based Feedback-RTO with «direct» constraint control
Process
Gradient estimator
Constraint controllers
(fast PID-controllers)
MAX/
MIN
y
g (measured constraint)
g (constraints paired with u1)
SP=0
u1
d
u2
Ju1
u1
Ju2
PID
u1o
SP=0
Ju1, Ju2 = NTJu (want=0), reduced gradients
(«self-optimizing variables»)
«Online Process Optimization with Active Constraint Set Changes using Simple Control Structure», D. Krishnamoorthy and S. Skogestad, I&EC Res., 2019
«Optimal controlled variables for ̈ polynomial systems». Jaschke, J.; Skogestad, S., J. Process Control, 2012
Selector on primal variables (inputs)
Similar to selectors in APC
Limitation: need to pair each constraint with an input u, may not work if many constraints
Feedback RTO
Define N as nullspace of active constraints
Optimality condition
Optimality condition becomes

## Slide 27
L. Bernadino, D. Krishnamoorthy and S. Skogestad, Comparison of Simple Feedback Control
Structures for Constrained Optimal Operation, Dycops-2022, IFAC PapersOnLine 55-7 (2022) 883–888
Feedback RTO

## Slide 28: Model-free optimization: Extremum Seeking Control (ESC) based on measuring cost J
Why ESC?
Expensive to obtain model (for J): Use data-based ESC instead of model-based RTO
May also be used on top of RTO
  «Adapt» setpoint for Ju (to a nonzero bias value) to correct for model error
  Aka «modifier adaptation»
Main problems with ESC:
Cost function J often not measured
  For chemical process J=pFF – pPP – pQQ
  need model (!) to estimate flows F, P and utility Q
Very slow. Typically 100 times slower than process dynamics

## Slide 29: Data-based optimization: “Hill-climbing” / “Extremum seeking control” Drive gradient Ju=dJ/du to zero.
Probe the system
Observe how the cost changes
Estimate Gradient
Decide which way to move
Ju=0 at top of hill

## Slide 30: Equivalent: Minimize cost J (go to bottom of valley)
uopt
Ju
0
Optimal setpoint: Ju=0
If Hessian Juu is constant:
  Ju as a function of u is a straight line with slope Juu
Nice properties for feedback control of Ju
No dynamics: Pure I-controller optimal
  SIMC-rule: KI = 1/(Juu τc)

## Slide 31: Classical Extremum seeking control using sinusoids
Gradient Estimation
I-controller
Multiplication trick: Draper & Li (1951)
Theory: Krstic & Wang (Automatica, 2000)
Process
u
uc
J
Simple to implement (don’t need computer), but
Prohibitively slow convergence for systems with slow dynamics
Typically 100 times slower than the system dynamics !
KI
Averaging
Remove bias in J
One side of optimum: Same phase
Other side: opposite phase

## Slide 32: More common today: Estimate Steady-state gradient using discrete perturbations (steps)
J
u
Usually only one input. Simplest: step change in u:
  Hill climbing control (Shinskey, 1967)
  Evolutionary operation (EVOP) (1960’s)
  NCO tracking (Francois & Bonvin, 2007)
  “Peturb and observe” = Maximum power point tracking (MPPT) (2010’s).
More advanced variants which may also be applied to multivariable systems
  Least squares estimation
  Fast Fourier transform (Dinesh Krishnamoorthy)
To avoid waiting for steady state
  Fitting of data to ARX model (difficult to make robust)
Note: Assumes steady state -> samling (step) time > 3-10 time process time constant

## Slide 33: Least square Extremum seeking control
LSE: Fit a linear model
Using least squares fit
Hunnekens et al. (2011, 2014)
Note: Assumes no dynamics -> samling time > 3-10 time process constant

## Slide 34: Summary extremum seeking control
Idea: Estimate the cost gradient Ju from data and drive it to zero
Common to all methods:
  Need measurement of cost J
  Must wait for steady state (except ARX method which fails frequently)
  Must assume no «fast» disturbances (while optimizing)
Algorithm needs two layers on top of process:
  1. Optimization layer (slowest): Drive Ju to zero (may use I-controller)
  2. Lower estimation layer: Estimate the local gradient Ju using data
    Must wait for the process to reach steady state
  Need time scale separation between layers.
    At best this means that the optimization needs to be 10 times slower than the process.
    Often it needs to be 100 times slower.
  Useful for fast processes with settling time a few seconds
  Not useful for many chemical processes where time constant typically are several minutes
    10 minutes * 100 = 1000 minutes = 16 hours
    Unllikely with 16 hours without disturbance

## Slide 35
ARC: Research tasks

## Slide 36
Complex optimal centralized Solution (EMPC, FL)
Sigurd
Present Academic control community fish pond
Simple solutions
that work (ARC, PID)
FL = feedback linearization

## Slide 37
Complex optimal centralized Solution (EMPC, FL)
Future Academic control community fish pond
Simple solutions
that work (SRC,PID)